## Slide 1
AI-Drievn Layout-Aware RTL Optimization Loop
Pipeline × Cognix
AI-Powered RTL Verification & Self-Optimizing
Cognix (ACI) | Hackathon 2026
TEAM MEMBERS :
Bhanuja Karumuru
Harshal Pimpalshende
Abhishek Bharadwaj
Saishruti Veda
https://github.com/Bhanuu01/AI-Drievn-Layout-Aware-RTL-Optimization-Loop.git

## Slide 2
Table of Contents
About the Project
3
The Problem
4
Our Solution
5
Pipeline Architecture
6
Why Now
7
Key Features
8
Demo & Results
9
Tech Stack
10
Roadmap
11

## Slide 3
About the Project
We build an AI-driven RTL verification and self-optimizing pipeline that automatically detects, diagnoses, and fixes hardware design bugs — reducing manual debug cycles from hours to seconds.
3
STAGES
Sim → Synth → Timing
AI
POWERED
Cognix (ACI) LLM Fixes
5ns
TARGET
Clock Constraint (200MHz)
Verilator
Yosys
OpenSTA
Cognix AI

## Slide 4
The Problem
SLOW, MANUAL, ERROR-PRONE LAYOUT DESIGNING
RTL engineers spend 60–70% of project time on debugging. Traditional flows rely on manual review of Verilator logs, Yosys reports, and STA output — disconnected tools with no automated remediation. Subsequently, the RTL codes usually do not have design fixes for some parameters that can be optimized in the code before handover to layout engineer.
No automated bug-fix loop
Timing violations caught too late
Context lost across tool boundaries
Repeated manual iteration cycles
Debug Time Breakdown
Simulation Debug
40%
Synthesis Review
20%
Timing Analysis
25%
Integration Fixes
15%

## Slide 5
Our Solution
AI Self-Optimizing RTL Pipeline
An automated pipeline that ties Verilator simulation, Yosys pre-synthesis, and OpenSTA timing analysis into a single loop — with Cognix AI generating and applying targeted RTL fixes at each failure point.
Auto-checks RTL + testbench files
Runs full 3-stage verification
Formats context-rich prompts for Cognix
Watches for file save → auto-reruns
Archives every successful run with logs
Sim Bugs Fixed
Verilator → Cognix loop
Synth Clean
Yosys latch/loop detection
Timing Met
STA WNS < −0.1 ns threshold

## Slide 6
Pipeline Architecture
📁
test/*.sv
RTL + TB Input
⚡
Verilator
Simulation
🔩
Yosys
Pre-Synthesis
⏱
OpenSTA
Timing STA
✓
✅ PASS
All Checks Done
AI FIX LOOPS
SIM FAIL → Cognix formats prompt with Verilator + Yosys logs → Apply fix → Re-run
SYNTH FAIL → Cognix gets Yosys blocking issue context → Fixes latches/loops → Re-run
TIMING FAIL → Cognix receives WNS/TNS + critical path → Restructures RTL → Re-run

## Slide 7
Why Now
The convergence of LLMs + open EDA tools makes this possible today.
LLMs Can Read Code
Models like Cognix understand SystemVerilog syntax, timing constraints, and synthesis semantics well enough to generate targeted RTL fixes.
Open EDA Maturity
Verilator, Yosys, and OpenSTA are now stable, scriptable, and freely available — enabling a fully automated verification chain.
AI-Native Dev Tools
IDE-integrated AI assistants (Cognix ACI) now support 'Apply' workflows, closing the loop between AI suggestion and file modification.
Hardware Complexity
SoC complexity is doubling every 2 years. Manual RTL debug is no longer sustainable — automation is a necessity, not a luxury.

## Slide 8
Key Features
Each feature purpose-built for real RTL design environments.
🔁
Auto-Detect Files
Scans test/ for RTL + TB, identifies top module automatically
🧠
Cognix AI Fix
Formats rich diagnostic prompts; watches for Apply → auto-reruns
🔩
Yosys Synthesis
Latch, loop, and multi-driver detection with netlist export
⏱
OpenSTA Timing
WNS/TNS analysis with critical path breakdown for targeted fix
📦
Run Archiving
Full logs, VCD, RTL snapshot archived per successful run
⚙️
CLI Configurable
--clock-period, --liberty, --skip-yosys and more flags
🔁
Layout Efficiency
Provides better design quality to ensure layout efficiency is relatively higher at the initial placement phase.
🔁
Project Duration
An optimized RTL code run through multiple iterations saves months of work.
🔁
Communication Pipeline
Acts as a direct pipeline to communicate between RTL Engineer and Layout Engineer.

## Slide 9
Demo & Results
Project Directories

## Slide 10
Demo & Results
Terminal Process
< 60s
Full Pipeline Run
Sim + Synth + Timing
5
Max Fix Iterations
Configurable via --max

## Slide 11
Demo & Results
WaveForm
WaveForm of “up_down_counter_tb”

## Slide 12
Tech Stack
SIMULATION
Verilator
--binary --timing --trace | SystemVerilog | VCD output
REQUIRED
PRE-SYNTHESIS
Yosys
read_verilog -sv | hierarchy -check | synth | check -assert
TIMING STA
OpenSTA
NanGate45 Liberty (auto-dl) | WNS/TNS | Critical path report
AI FIX ENGINE
Cognix (ACI)
Context-rich prompts | ACI Apply button | File-watch loop
REQUIRED
LANGUAGE
Python 3.10+
subprocess | pathlib | watchdog | argparse | json logging
REQUIRED
HDL
SystemVerilog
RTL + Testbench (.sv) | $dumpfile/$dumpvars | $finish
REQUIRED
Optional
Optional

## Slide 13
Future Scope
Phase 1
If Cognix API is provided, the flow of RTL codes can be automated.
Minimizes the necessity of manual labour which is tedious and significantly slower and less efficient.
MCMM Timing Awareness - AI optimizes RTL across multiple PVT timing corners
Design Space Exploration (DSE) - AI evaluates architectures for latency, area, throughput
Explainable AI Debugging - Generates explanations for every RTL code fix
Mixed-Signal Co-Simulation Support - Integrates Verilog-AMS/SystemC for SoC debugging
CI/CD Hardware Integration - Automates RTL validation during design commits
FPGA-in-the-Loop Validation - Tests AI-modified RTL on FPGA hardware
Phase 2
Analysis tools shall be integrated into this to perform analysis for pre-layout quality checks.
Thereby, partial layout quality improvement is done without even reaching layout phase.
Phase 3
Cognix then becomes a smart assistant to layout engineers as they progress to generate netlist on tools such as Cadence Genus.
Following that, Layout can be designed on tools such as Cadence Innovus.
Further verification steps performed using tools such as Cadence Tempus, Pegasus and Quantus for full Signoff.
Phase 4
Repeat the process on multiple designs.
Run comparison tests proving how the addition of AI to semiconductor design is a massive boost to manufacturing thereby cutting the shortage globally.
Subsequently figure out techniques to allow for layout engineers to verify and adopt possible designs using the help of AI using layout placement ideas.
All these steps will require funding and support from Cognichip AI.

## Slide 14
Thank You
AI-Driven Layout-Aware RTL Optimization Loop
Hackathon 2026